## Slide 1: Supporting Real Time Application in an Integrated Services Packet Network: Architecture and Mechanism
Presented by,
Debolina Halder Lina
T00307622

## Slide 2: Overview
Real-time application
Key component of ISPN architecture
Service commitments
Scheduling algorithms
Service interface
Admission control
Other service qualities
Final thoughts

## Slide 3: What is real time application?
A real-time application (RTA) is an application program that functions within a time frame that the user senses as immediate or current.

## Slide 4: Properties of real time traffic
Play-back application
Source takes some signal, packetizes it and transmits it over the network
Network introduces variation in the delay of each packet – jitter
Receiver depacketizes the signal and tries to play back
Play back point
Sensitive to data delivery delay

## Slide 5: The Nature of Delay
Delay in transmission at each switch point waiting for the entire packet to arrive (fixed)
Time that each packet spends in the service queue (variable)
Real time sources can be bursty
Statistical sharing

## Slide 6: Dealing with Delay
Rigid vs Adoptive application
Tolerant and intolerant network client

## Slide 7: 4 Key Component of ISPN Architecture
Nature of commitment made by the network
Service interface
Packet scheduling behavior of network switches
Means by which the traffic and service commitments get established

## Slide 8: Service Commitments
Guaranteed service commitment
  Depends on no other assumptions
  If the network Hardware is functioning and the client is conforming to its traffic characterization, service commitment will be met
  Appropriate for intolerant and rigid client
Predicted Service Commitment
  Appropriate for tolerant and adaptive client
  Assumes that upcoming flow will be similar to present flow.
  Adjust their playback point to reflect the delays their packets are currently receiving
Datagram Traffic
  Makes no service commitment
  Promises not to delay or drop any packet unnecessarily.

## Slide 9: Scheduling Algorithms
Scheduling algorithm for guaranteed traffic
Scheduling algorithm for predicted traffic
Unified scheduling algorithm

## Slide 10: Scheduling Algorithm for Guaranteed Traffic
WFQ algorithm

## Slide 11: Scheduling Algorithm for Predicted Traffic
What will happen when all sources are transmitting uniformly except for one which emits a burst of packets?
What will happen if we use FIFO in place of WFQ?
WFQ focuses on isolation, FIFO focuses on sharing
Priority is a midway
Multi hop sharing (FIFO+)

## Slide 12: Unified Scheduling Algorithm
Have to isolate guaranteed service flow from predicted and datagram flow
Time stamp based WFQ
Each guaranteed service client has a separate WFQ flow and all the predicted service and datagram service is assigned to a pseudo WFQ flow(flow 0)
Inside flow 0, there are a number of strict priority classes
Within each priority class, FIFO+ algorithm is performed
After assigning each predicted service flow (and data flow) to a priority level at each switch, the scheduling algorithm is completely defined

## Slide 13: Unified Scheduling Algorithm
Datagram traffic is assigned to the lowest priority class
There are K other priority levels and K widely spaced target delay bound for predicted traffic

## Slide 14: Service Interface
For guaranteed service, the source needs to specify it’s needed clock rate and the network guarantees this rate
For predicted service, the service interface much characterize both service ( suitable delay and target loss rate the application can tolerate) and traffic (token bucket filter).
Each predicted service flow is checked at the edge of the network for conformance to its declared token bucket filter
In case of predicted service, the token bucket helps the flow admission control computation

## Slide 15: Admission Control
The datagram traffic must have access to at least 10% of bandwidth
The addition of a flow should not increase any of the predicted delays

## Slide 16: Other service Qualities
If overload causes some of the packets from a source to miss their deadline, the source should be able to separate its packets into different classes, to control which packets get dropped.
Packets that are sufficiently late should be discarded internally, rather than being delivered
Packets should be buffered in the network if they might otherwise arrive early

## Slide 17: Final Thoughts
The language is hard
Background can be discussed earlier
They developed the algorithm on the assumption that there will be two dominant classes of traffic in the network – intolerant and rigid client and tolerate and adaptive client
Validation of their proposal rested on their ability to formulate an admission control policy which will make the predicted service class sufficiently reliable.
They mentioned some service qualities but didn’t describe properly how to support them in their proposed context
They mentioned in the paper that determining how to evaluate their proposal is challenging because it needs to be tested in a dynamic environment with adoptive clients